## Slide 1: MMC vs MNA prof. Joseph MORLIER phd candidate Simone CONIGLIO school referent: Miguel CHARLOTTE Herraz Mahfoud

## Slide 2: Explicit vs Implicit topology optimization
Explicit (MMC, MNA)
geometrical design variables
Structure’s shape directly determined from design variables
Implicit (SIMP, level set method)
density variables/nodal value of implicit function
Structure’s shape determined via density field (or level set function)
(GUO et al. 2015) A new topology optimization approach based on Moving Morphable Components (MMC) and the ersatz material model

## Slide 3: Pros and Cons (Implicit)
Advantages
Cheap sensitivities
Adapted for MMA optimizer
Better control of density field
Drawbacks
High mesh dependency
Numerical instabilities (checkerboard patterns)
Post-processing needed for CAD design
High resolution increases design variables number

## Slide 4: Pros and Cons (Explicit)
Advantages
Adapted for CAD
Small number of design variables
Less mesh dependency (no filtering)
Resolution and variables number independent
Drawbacks
Expensive sensitivities:
Solution depends on initial number of components
Optimization problem is more nonlinear
Less control over the structure’s shape (density field)

## Slide 5: MMC scheme
Design is achieved through layout of a set of components
Design variables for a components
The contribution of one component is described by it’s topology description function (TDF):
withandlocal coordinates of current pointdepend on design variables
(Guo et al. 2014) Doing Topology Optimization Explicitly and Geometrically-A New Moving Morphable Components Based Framework

## Slide 6: MMC scheme
design vector, the structure is described by the union of topology description functions (TDFs) of all components:
Nodal density field: where is the regularized Heaviside function:
(Guo et al. 2014) Doing Topology Optimization Explicitly and Geometrically-A New Moving Morphable Components Based Framework

## Slide 7: MNA scheme
Design is achieved through layout of a set of components
Design variables for a components
Density field of a component

## Slide 8: Difference with MNA
the main difference : the weight function allows more gray regions (intermediate densities) which is not the case of the regularized Heaviside function
Consequences:
Better and easier convergence
Better control over the structure’s shape
Design gets connected quickly
Structure become disconnected progressively

## Slide 9: Difference with MNA
Justification
More gray regions in MNA
 bigger components for same volume
Components can intersect each other quickly and easily
structure get connected in MNA quicker and easier than MMC

## Slide 10: Difference with MNA
Justification
Initial disconnected design:
In order to connect it: lengths and thicknesses are increasing (higher gradients)
Components position doesn’t change
Strong variations in compliance and volume

## Slide 11: Difference with MNA
Justification
Presence of gray regions in MNA:
Compliance and volume’s variation with respect to design variables are :
Smooth in MNA
Non smooth in MMC
 Better convergence finding minimum is easier with MNA

## Slide 12: Extension to curved components
Introducing a new design variable : curvature
Need for basis change :
 from global to local (center of component) basis :
 if
translation from local to curvature center
Cartesian to polar coordinates

## Slide 13: Cantilever beam
Mesh: 80x40
Formulation:
Volfrac: 0,4
Tolerances: 0,001 for change & 0,01 for KKT norm
Maximum iteration number: 600
DH=1
DW=2
F=1
Original MMC code
Compliance: 74,68
224 design variable
CPU time/iteration: 0,224s
Enhanced MMC code
Compliance: 73,9
224 design variable
CPU time/iteration: 0,29s
MMC with curvature
Compliance: 75,08
192 design variable
CPU time/iteration: 0,228s
MNA code
Compliance: 78
160 design variable
CPU time/iteration: 0,3
SIMP (top88mma)
Compliance: 80,06
3200 design variable
CPU time/iteration: 0,37s

## Slide 14: MBB beam
Mesh: 80x40
Formulation:
Volfrac: 0,4
Tolerances: 0,001 for change, 0,01 for KKT
Maximum iteration number: 600
DH=1
DW=2
Original MMC code
Compliance: 97
224 design variable
CPU time/iteration: 0,242s
Enhanced MMC code
Compliance: 91,19
224 design variable
CPU time/iteration: 0,29s
MMC with curvature
Compliance: 91,6
192 design variable
CPU time/iteration: 0,226s
MNA code
Compliance: 95,8
160 design variable
CPU time/iteration: 0,33
SIMP (top88mma)
Compliance: 97,66
3200 design variable
CPU time/iteration: 0,34s

## Slide 15: L-shape beam
Mesh: 80x80
Formulation:
Volfrac: 0,4*0,75
Tolerances: change:0,001 KKT:0,01(MMC) 0,002(MNA)
Maximum iteration number: 600
F=1
Original MMC code
Compliance: 98,16
336 design variable
CPU time/iteration: 0,57s
Enhanced MMC code
Compliance: 97,42
336 design variable
CPU time/iteration: 0,75s
MMC with curvature
Compliance: 96,9
288 design variable
CPU time/iteration: 0,59s
MNA code
Compliance: 97,15
325 design variable
CPU time/iteration: 0,53s
SIMP (top88mma)
Compliance: 96,66
3200 design variable
CPU time/iteration: 0,386s

## Slide 16: Pylon architecture (airbus project)
Initial design
 | SIMP | MNA
Compliance | 7123 | 5105
Volume | 0,109 (unsatisfied) | 0,1 (satisfied)
TSFC | 0,15 (satisfied) | 0,149 (satisfied)
Stress | -0,016 (satisfied) | -0,031 (satisfied)
Iterations | 400 | 400
Time/iteration | 4,5 | 8s
Design variables | 7600 | 5x5x5x9=1125
Components plot
Density field MNA
Density field SIMP

## Slide 17: Conclusion
Enhanced MMC code is more efficient
Curved components show good results and enrich MMC formulation
MMC has more ability to explore design domain and leaves local optimums easier than MNA
MMC is very accurate and gives good results but very sensitive to optimizer parameters and initial configuration
In MNA: less need for tuning, much less sensitive to initial point
MNA worked for all test cases but not MMC!

## Slide 18: Limitations/Perspectives
LIMITATIONS
More complex geometry description
Gradient based methods  risk of finding local optimum
Gray regions can remain if not enough components used
PERSPECTIVES
Implement analytical gradients
Implement MMC efficiently for 3D airbus case (irregular mesh)
Improve the components plot given by MNA